## Slide 1
LHC Status & Plans

## Slide 2: Integrated pp luminosity 2010-12
2010 : Ecm=7 TeV
L=0.04 fb-1
2011 : Ecm=7 TeV
L=6.1fb-1
2012 : Ecm=8 TeV
L=23.3 fb-1

## Slide 3: Performance through the year
 | 2010 | 2011 | 2012 | Nominal
bunch spacing [ns] | 150 | 50 | 50 | 25
no. of bunches | 368 | 1380 | 1380 | 2808
beta* [m] ATLAS and CMS | 3.5 | 1.0 | 0.6 | 0.55
max. bunch intensity [protons/bunch] | 1.2 x 1011 | 1.45 x 1011 | 1.7 x 1011 | 1.15 x 1011
normalized emittance [mm-mrad] | ~2.0 | ~2.4 | ~2.5 | 3.75
peak luminosity [cm-2s-1] | 2.1 x 1032 | 3.7 x 1033 | 7.7 x 1033 | 1.0 x 1034
>2x design when scaled to 7 TeV!

## Slide 4: A challenge in RUN-I - pile up events
ATLAS
Z μμ event from 2012 data with 25 reconstructed vertices
2012
2011
pile up will increase at higher energy →
experiments request 25 ns operation
in 2015

## Slide 5: Operational cycle
turn around 2 to 3 hours on a good day
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours

## Slide 6: LHCb
luminosity leveling at around 41032 cm-2s-1 via transverse separation (with a tilted crossing angle)

## Slide 7: Run-II: 2015
energy: 6.5 TeV (magnet retraining)
bunch spacing: 25 ns
  pile-up considerations
injectors potentially able to offer nominal intensity with even lower emittance
uncertainties for 2015:
  electron cloud
  UFOs
both get more difficult at 25 ns & at higher energy
energy (limited by retraining)
 | Number of bunches | Ib LHC FT[1e11] | Emit LHC [um] | Peak Lumi [cm-2s-1] | ~Pile-up | Int. Lumi per year [fb-1]
25 ns low emit | 2520 | 1.15 | 1.9 | 1.7e34 | 52 | ~45
expected maximum luminosity from inner triplet heat load (collisions debris) 1.7×10 34 cm-2s-1 ±20%

## Slide 8: draft 2015 shedule
in red beam time requested by LHCf

## Slide 9: Plan for next 10 years

## Slide 10: Luminosity forecast for next 10 years
~30/fb at 3.5 & 4 TeV
~400/fb at 6.5-7 TeV
~3000/fb at 7 TeV
to obtain 3000/fb by 2035
we need the HL-LHC
2012 DONE
2021 goal (?)
2035 goal (??)